Handmade Processor
Dino Filipovic (dino.filipovic@vanderbilt.edu)
Project Description
This project involves the physical construction of a processor architecture on breadboards. The core computational unit is a custom Arithmetic Logic Unit (ALU) constructed from fundemental logic gates (SN74HC00N NAND, SN74HC86N XOR), enabling 4-bit addition, subtraction, and iterative shift-add multiplication operations. Data storage is managed by a register file built from D-type flip-flops (SN74HC74N), with input/output multiplexing handled by SN74HC157N ICs.
Objectives and Goals
1. Synthesize the arithmetic logic unit from a gate level with a main ripple-carry adder. Multiplication is implemented using the ALU and registers using a shift-add algorithm.
2. The control unit is constructed from flip-flops and allows the neccessary control signals to execute operations over multiple clock cycles.
3. Contents of registers should be visually indicated in real-time via LEDs, providing direct insight into the operation of hte processor.
General Timeline for Project

Date	What should be done?
10-30	Design Finalized and parts ordered
11-14	Construction Finished and final debugging
11-17	Showcase

Specifications (like price estimates and certain aspects the product should be achieving)
- We estimate that the project’s expenses will be between $80 to $100.
- 4 bit logic should be implemented and operations should execute in an expected way so that the processors interface could be usable by other componoents.